## Slide 1: RS232 & RS485

## Slide 2: Q: 1 The maximum length of RS-232 cable is 50ft
The length of wire is based on its resistance value. The resistance value of RS232 is 3K- 7K
If resistance is more than the range (3K – 7K) then the data will be loss.
The receiver cannot receive the actual data from transmitter.

## Slide 3: Q 2: The maximum length of RS485 cable is 4000 feet
If we need transfer data above 4000 feet we need to connect another RS485 repeater .

## Slide 4: Q 3 : what is single ended and differential(multi drop)
Single ended mode one pin is connected with signal another pin is connected with ground if we send 10 signals means we need 11 conductors (wires) . One is for ground remaining is for each signal(10)
Differential signalling, which is less common than single-ended signalling, employs two complementary voltage signals in order to transmit one information signal. So one information signal requires a pair of conductors; one carries the signal(positive signal) and the other carries the inverted signal( negative signal)

## Slide 5: Q 4: less susceptible to noise issues
Electric noise can cause all kinds of problem for electronics.
RS485 avoid this issue which also allows for shielding of cables to prevent noise.
If noise increased we cannot get the actual data .

## Slide 6: Q5 : RS232 concept
We can send and receive the data at a time (full duplex mode)
Only in loopback method we can send data one time and receive data another time.
we cannot receive and send at a time(loop back method)

## Slide 7: Q6 : What is Noise
An undesirable electrical signal—Noise comes from external sources such as the AC power line, motors, generators, transformers, fluorescent lights, CRT displays, computers, electrical storms, welders, radio transmitters, and internal sources such as semiconductors, resistors, and capacitors. Noise corrupts signals when we were trying to send or receive.